## Slide 1: CrypTech
Building a More Assured
HSM Design
Randy Bush <randy@psg.com>
Notes: A stuffed teddy bear to the person who thinks of a better name

## Slide 2: Built on the Beltway & GCHQ
Where Keys Go to Hide
A Black Box Governments Certify You Can Trust

## Slide 3: Post Snowden, No One Trusts Them We are relying on HSMs designed and made by 42-eyes government contractors

## Slide 4: Broken Despite Gov Issued CC Evaluation & NIST FIPS 140-2 Validation

## Slide 5: Origins
This effort was started at the suggestion of Russ Housley, Jari Arkko, and Stephen Farrell of the IETF, to meet the assurance needs of supporting IETF protocols in an open and transparent manner.
But this is NOT an IETF, ISOC, ... project, though both contribute. As the saying goes, “We work for the Internet.”

## Slide 6: Goals
An open-source reference design for HSMs, not a manufactured product
Scalable, first cut in an FPGA and CPU, plan higher speed (ASIC)options later
Composable, e.g. “Give me a key store and signer suitable for DNSsec”
Reasonable assurance by being open, diverse design team, and an increasingly assured tool-chain

## Slide 7: CrypTech Project
An Open Design, not a Product
Open – everything (docs, design, code)
BSD, CC license for all we develop
Diverse engineers and review
Support for transparency, testing, …
Multiple contributors: IETF, Comcast, Google, .SE, SUNET, PIR, ISOC, Afilias, RIPE, IANA, etc.

## Slide 8: Layer Cake Model
FPGA (ASIC)
Hashes: SHA*/GOST Encrypt: AES/Camellia PublicKey RSA/ECC/DSA, Block Crypto Modes
TRNG, BigNum, Modular, Exponentiation
On-Chip Core(s)
KeyGen/Store, Hash, Sign, Verify, Encrypt, Decrypt, DH, ECDH,
PKCS#1/5/8, [Un]Load, Stretching, Device Activation/Wipe
Off-ChipSupport Code
X.509/PGP/… Packaging, PKCS#7/10/11/15, Backup
Applications
DNSSEC, RPKI, PGP, VPN, OTR, random, TCP/AO, …
Security
Boundary
&
Tamper
Power
Timing

## Slide 9: Status Overview
State of the Art TRNG with Entropy from Avalanche & on-FPGA RingOscs
Hashes: SHA-2, SHA-256, SHA-512, SHA-512x
Stream Cipher: ChaCha
AES-128 & AES-256 (RSA Started)
BigNum and Modular Exponentiation
DNSsec Signing Summer 2015

## Slide 10: Proto on Novena Summer ‘15
FPGA

## Slide 11: Alpha Board EOY 2015

## Slide 12: Funding From
A Few Private Donations