What is an FPGA?
Large matrix of flip-flops and look-up tables
Flip-flips (aka registers) store bits of data
Look-up tables form Boolean logic functions
Configurable I/O pins
Clocking backbone
Programmable interconnect

---
FPGA Design Example
// Verilog source for 4-bit counter
module cnt4(clk, rst_n, dout);
input wire clk;
input wire rst_n;
output reg [3:0] dout;
always @(posedge clk or negedge rst_n)
if (rst_n == 1'b0)	dout <= 4'h0;
else	dout <= dout + 1'b1;
endmodule

---
Synthesized
4-bit counter

---
Synthesized
4-bit counter
Flip-flops

---
Synthesized
4-bit counter
Flip-flops
Look-up tables

---
Synthesized
4-bit counter
Flip-flops
Look-up tables
I/O pins

---
Synthesized
4-bit counter
Flip-flops
Look-up tables
I/O pins
Flexible interconnect

---
Synthesized
4-bit counter
Flip-flops
Look-up tables
I/O pins
Flexible interconnect
Clocking backbone

---
Synthesized
4-bit counter
Flip-flops
Look-up tables
I/O pins
Flexible interconnect
Clocking backbone
PLLs (clock synthesizers)
Block RAM
DSP blocks

---
Why need an FPGA?
More resistant to common side-channel attacks against crypto hardware
    - True constant-time-by-design implementation is possible
    - Absense of data-dependent behaviour
More robust implementation of crypto algorithms
  - No stack overflows
  - No dynamic memory allocations, no pointers
  - Physical isolation of cores

---
Why need an FPGA?
High performance
  - Processors are typically optimized for instruction throughput
  - FPGAs are not optimized per se, users can set their own optimization goals
  - Very linear speed/space tradeoff
Intermediate step towards an ASIC
  - C implementation of reference model
  - HDL implementation
  - Verification in simulator using testbenches
  - Verification in hardware using FPGA
  - ASIC implementation

---
Alpha Board FPGA
XC7A200T from Xilinx (Artix-7 Family)
  - 270k LUTs, 135k FFs
  - 13 Mb of block memory, 740 DSP blocks
  - average price: 190$ (-1 speed grade)
- Pin-compatible alternative: XC7A100T
  - 50% smaller
  - average price: 140$

---
CrypTech FPGA Cores
Available cores
  - AES, ChaCha
  - SHA-1, SHA-2, SHA-3
  - RSA (Modular Exponentiation)
  - Entropy source for the TRNG
  - MKM Interface
  - GOST R 34.11-2012 (aka Streebog)

---
CrypTech FPGA Cores
Cores being developed
  - ECDSA (curves P-256 & P-384, DNSSEC algorithms 13 & 14)

---
CrypTech FPGA Cores
Planned cores
  - GOST R 34.10-2001 (aka ECC-GOST, DNSSEC algorithm 12)
  - Curve25519 / Ed25519
  - ...